## Slide 1: Ion University: Technology Ion Chef & OT2 w/ S5™ & S5xl™
July 2016
Robert David, Staff Field Applications Specialist

## Slide 2: S5 XL System Operations Training Agenda
Ion University
  Overview of Ion Torrent Sequencing technology and Primary data analysis
Hands-on training
  Library Preparation on the Ion Chef
  Template Preparation & Chip Loading on the Ion Chef™
    Clonal Amplification
    Recovery
    Enrichment, QC option
    Chip loading
  Sequencing on the S5™ XL
Discussion
  Library Preparation
  Data Analysis

## Slide 3: Our Enduring Belief that Ion is Disruptive
Generations are defined by who can use them.
Main Frame
Mini Computer
Personal Computer
Sanger Sequencing
Next-Gen Sequencing
Ion Semiconductor Sequencing

## Slide 4: Founding Principles of Ion Torrent
  CMOS technology
  40 years of Moore’s law
  Natural nucleotides
  No lasers
  No optics
  No camera
  No fluorescence
  No enzyme cascade
  Rapid detection of sequence extension

## Slide 5: Semiconductor Technology
Wafer
Chip Cross Section
Chip
Notes: Wafer – the semiconductor material. Serves as the substrate for microelectronic devices.
Chip – has a flowcell on top of it to deposit the sample.
Cross – section – sensor layer of the chip where a change in pH ultimately measures a change in voltage and then turned into Base Calls (fastq files)
Complementary metal–oxide–semiconductor (CMOS) is a technology for constructing integrated circuits.
No Lasers, Fluoresnce, optics, cameras etc.
Rapid detection of sequence extension

## Slide 6: Natural Chemistry
  Natural nucleotides
  No lasers
  No optics
  No camera
  No fluorescence
  No enzyme cascade
Notes: Main idea here is the chemistry is “natural” in the sense that we don’t modify the dNTPs. When we flow 1 dNTP at a time, if there is an incorporation, a hydrogen ion is released on each template on the Ion Sphere Particle (only one shown here). This release of H+ causes a change in the pH of the well that is detected by our “ion sensitive layer” at the bottom of each well. So the signal we detect is caused by an incorporation event, and we know what dNTP we were flowing at that time, so we infer what base was on the template. If no signal is detected (other than background) we assume no incorporation during that dNTP flow.

## Slide 7: Fast Direct Detection
DNA  Ions  Sequence
  Nucleotides flow sequentially over Ion semiconductor chip
  One sensor per well per sequencing reaction
  Direct detection of natural DNA extension
  Millions of sequencing reactions per chip
  Fast cycle time, real time detection
Rothberg J.M. et al Nature doi:10.1038/nature10242
Sensor Plate
Silicon Substrate
Drain
Source
Bulk
dNTP
To column
receiver
∆ pH
∆ Q
∆ V
Sensing Layer
H+
ISP
Notes: Speed
  Rapid detection of sequence extension
Schematic representation of one microwell on the surface of a chip
  High signal to noise
  Enables high raw accuracy
  One sensor per well per sequencing reaction
Orange circle is an Ion Sphere Particle onto which is clonally amplified the sequence fragment resulting from library preparation or amplicon PCR
Release of H+ ions as nucs incorporate generates a pH change inside the well which in turn causes charge accumulation in the Ion sensitive layer which then in turn causes a voltage increase mediated through the transistors directly underneath each well. Voltage signals are turned into base calls and output either as Ionograms (SFF files) or bases (FastQ) files
Sample at variable frame rate across pre-wash, nuc-flow, and post-wash

## Slide 8: Applications
Ion S5 and Ion S5 XL Systems
Simplest NGS targeted workflow - <45mins total hands-on time from DNA to data with Ion Chef™ System
Fastest run time – as little as 3.5 hours from sequence to BAM files.
Lowest capital investment - Single platform for all targeted applications with flexibility to scale
Lowest DNA/RNA input requirements – 1-10ng using Ion AmpliSeq™ technology
Easy setup and training – single day installation and plug and play cartridge-based reagents
Simplest and fastest targeted sequencing system
with the lowest capital investment

## Slide 9: Ion S5™ and S5™ XL Systems.

## Slide 10: Ion S5 and Ion S5 XL Systems Sequence up to 15 Gb in < 8 hours
 | 200bp Sequencing Time Ion S5/S5 XL | 200bp Analysis Time* Ion S5 XL | 200bp Analysis Time* Ion S5 | Output | Reads | Read Length
Analysis time to BAM file
Ion 530 Chip | 2.5 hr | ~2.5 hr | ~8 hr | 3-5 Gb | 15-20 M | Up to 400bp
Ion 540 Chip | 2.5 hr | ~5 hr | ~16.5 hr | 10-15 Gb | 60-80 M | Up to 200bp
Ion 520 Chip | 2.5 hr | ~1 hr | ~5 hr | 1-2 Gb | 3-5 M | Up to 400bp
Rapid time to answer
Affordable flexibility
Notes: 520 is 318 equivalent
540 is PI equivalent

## Slide 11: Ion Torrent Workflow
Library
Preparation
Sequencing*
Data Analysis
Template Preparation*
Notes: Set expectations of the class:
There are several parts of the Ion workflow. The important phases are broken u here. The parts in blue we will go over in the lab together. This course does not cover the Library Prep portion of the workflow but we do offer several courses which cover this portion of the workflow.

## Slide 12: Ion Workflow Overview
Data Analysis
Clonal
Amplification
Isolate Positive
Ion Sphere™
Particles
Load Chip
and Sequence
Prepare
Library
10
10
DNA
A
Sequencing
D
Template Prep
C
Compatible Library Prep
B
Compatible Data
E
Notes: Ion Torrent Systems, Inc.
12

## Slide 13: Ion Workflow – Library Preparation
gDNA /
Long Amplicon
Libraries
Fragmentation
(Size dependent)
End Repair
(for physical
shearing)
Adapter Ligation
/ Nick repair
Size selection
Amplification*
(if needed)
Qualify &
Quantify
~2-3 hrs
Short Amplicon
Libraries
PCR
Clean Up
Quantification
~3 hrs
Ion RNA
Libraries
Prepare WT
or miRNA
Hybridization /
Adapter Ligation
Reverse
transcription
Size selection
Amplification
Qualify &
Quantify
~5-6 hrs
*extra option: Ion Library Equalizer™ Kit
Ion AmpliSeq™
RNA Libraries
Multiplex
PCR
Digest Primers
Adapter
Ligation
Purify
Amplification
Qualify &
Quantify
~5 hrs
Reverse
Transcript-
ion
Ion AmpliSeq™
(DNA) Libraries
Multiplex
PCR
Digest Primers,
Phosphorylate
Adapter
Ligation
Purify
Qualify &
Quantify
~3.5 hrs
Amplification*
(if needed)
Library Preparation
Sequencing*
Data Analysis
Template Preparation*
Notes: Many application specific Library Prep protocols to chose from.
For examples RNA or DNA, Frag, Ampliseq or RT workflows. Note all are less than 1 day and all share several steps. Varied workfows for all customers
Emphsize Ion AmpliSeq libraries.

## Slide 14
Ion AmpliSeq™ DNA Library Prep
  Design your own with AmpliSeqTM Designer
  Fast library Prep
  Ultrahigh multiplex options

## Slide 15: High Level Workflow Comparison

## Slide 16: Ion Torrent Workflow
Library
Preparation
Sequencing*
Data Analysis
Template Preparation*
Notes: Set expectations of the class:
There are several parts of the Ion workflow. The important phases are broken u here. The parts in blue we will go over in the lab together. This course does not cover the Library Prep portion of the workflow but we do offer several courses which cover this portion of the workflow.

## Slide 17: Ion Workflow Overview
Data Analysis
Clonal
Amplification
Isolate Positive
Ion Sphere™
Particles
Load Chip
and Sequence
Prepare
Library
10
10
DNA
A
Sequencing
D
Template Prep
C
Compatible Library Prep
B
Compatible Data
E
Notes: Ion Torrent Systems, Inc.
17

## Slide 18: Two options for Template Prep Workflow
Library Preparation
Sequencing*
Data Analysis
Template Preparation*
Template Prep Enrichment
Template Prep , Enrichment & Loading
OneTouch2TM ES
Ion Chef TM

## Slide 19: Clonal Amplification
Notes: Introduce the idea of an emulsion.

## Slide 20: Ideal Clonal Amplification

## Slide 21: Non-Ideal Amplification
Amplification
“mixed” reads
duplicate reads
“Non-productive”

## Slide 22: Input Optimization
Optimizing the library input concentration
Amplification
Low DNA
High DNA
Increasing [DNA]
“Mixed” read
No read
Optimal DNA
Too little library input can result in
insufficient positive,
or “live”, spheres for sequencing
Too much library input to
template prep can result in
too many “mixed” reads

## Slide 23: Input Optimization
% Mixed Reads
System Throughput
Optimal Range
Optimal DNA input will maximize system throughput
DNA Concentration

## Slide 24: Ion Sphere™ Particle Enrichment
Post
Amplification
Add Magnetic
Streptavidin Bead
Immobilize to
Magnet and Wash
Remove 2nd strand
with NaOH
SA
SA
SA
Enriched
ISP
SA
SA
“no template”
“no biotin” “no capture” “no yield”
Notes: Addition of MyOne™ beads to sample to bind to biotinylated templated ISPS.
Washing
Magnetic purification
Melting Off
Recovery of template positive ISPs.

## Slide 25: Ion Sphere™ Particle Enrichment (mixed reads)
Post
Amplification
Add Magnetic
Streptavidin Bead
Immobilize to
Magnet and Wash
Melting off 2nd strand
with NaOH
*This mixed read species can be minimized through proper dilution.
Proper DNA to Ion Sphere™ Particle ratio is critical!
SA
SA
SA
Notes: Note that enrichment does not remove ‘mixed’ or ‘polyclonal’ ISPs. Those must be minimized via dilution in the template prep.

## Slide 26: Ion Torrent™ Workflow
Library
Preparation
Sequencing*
Data Analysis
Template Preparation*
Notes: Set expectations of the class:
There are several parts of the Ion workflow. The important phases are broken u here. The parts in blue we will go over in the lab together. This course does not cover the Library Prep portion of the workflow but we do offer several courses which cover this portion of the workflow.

## Slide 27: Ion Workflow Overview
Data Analysis
Clonal
Amplification
Isolate Positive
Ion Sphere™
Particles
Load Chip
and Sequence
Prepare
Library
10
10
DNA
A
Sequencing
D
Template Prep
C
Compatible Library Prep
B
Compatible Data
E
Notes: Ion Torrent Systems, Inc.
27

## Slide 28: Sequencing: Flows
3’-CCATCTCATCCCTGCGTGTCTCCGAC A G T C A A G C G T C C C A T G
T
A
C
G
T
A
C
G
T
Flows 1-4
…9-12
Flows 5-8
… etc.
T
A
C
G
Flows 1-4
...---Ion Sphere™
Particle
A “flow” is the event of exposing the chip to one particular dNTP (T, A, C, or G), followed by a washing step
The flow order repeats with pattern:
  ‘TACGTACGTCTGAGCATCGATCGATGTACAGC’
C
G
A
C
G
T
A
C
G
T
A
Adaptator A
Key Seq
Sequence of Interest
P1 seq
5’-Sequencing Primer-3’
Notes: HOW DO WE DEAL WITH SAMBA? NEED TO THINK ABOUT THIS AS WE DON’T WANT TO DRAW TONS OF ATTENTION TO FLOW ORDER BUT THIS CONCEPT IS IMPORTANT.
Focus on the following: The key flows are important for recognizing the type of ISP (library or control) and for identifying what a signal of “1” looks like. After that, the flow order really doesn’t matter – just show them we are sequencing by synthesis, in towards the ISP, sometimes incorporating 0 bases, 1 base, or several bases per flow.
Ion Torrent Systems, Inc.
2/2/2017
28

## Slide 29: Sequencing: Flows
T
A “flow” is the event of exposing the chip to one particular dNTP (T, A, C, or G), followed by a washing step
The flow order repeats with pattern:
  ‘TACGTACGTCTGAGCATCGATCGATGTACAGC’
3’-CCATCTCATCCCTGCGTGTCTCCGAC A G T C A A G C G T C C C A T G
C
T
A
C
G
T
A
C
G
T
Flows 1-4
…9-12
Flows 5-8
… etc.
T
A
C
G
Flows 5-8
...---Ion Sphere™
Particle
C
G
A
C
G
T
A
C
G
T
A
Adaptator A
Key Seq
Sequence of Interest
P1 seq
5’-Sequencing Primer-3’
Notes: Ion Torrent Systems, Inc.
2/2/2017
29

## Slide 30: Sequencing: Flows
T
C
T
A
C
G
T
A
C
G
T
C
G
A
C
G
T
A
C
G
Flows 1-4
…9-12
Flows 5-8
… etc.
T
C
G
T
Flows 9+
A
G
...---Ion Sphere™
Particle
A “flow” is the event of exposing the chip to one particular dNTP (T, A, C, or G), followed by a washing step
The flow order repeats with pattern:
  ‘TACGTACGTCTGAGCATCGATCGATGTACAGC’
T
T
A
3’-CCATCTCATCCCTGCGTGTCTCCGAC A G T C A A G C G T C C C A T G
Adaptator A
Key Seq
Sequence of Interest
P1 seq
5’-Sequencing Primer-3’
Notes: Ion Torrent Systems, Inc.
2/2/2017
30

## Slide 31: Sequencing: Flows
T
A
C
G
T
A
C
G
T
A
C
G
T
Flows 1-4
…9-12
Flow 5-8
… etc.
T
A
C
G
T
T
T
C
G
C
A
G
G
G
T
A
C
And so on…
...---Ion Sphere™
Particle
A “flow” is the event of exposing the chip to one particular dNTP (T, A, C, or G), followed by a washing step
The flow order repeats with pattern:
  ‘TACGTACGTCTGAGCATCGATCGATGTACAGC’
C
G
A
C
G
T
A
C
G
T
A
3’-CCATCTCATCCCTGCGTGTCTCCGAC A G T C A A G C G T C C C A T G
Adaptor A
Key Seq
Sequence of Interest
P1 seq
5’-Sequencing Primer-3’
Notes: Ion Torrent Systems, Inc.
2/2/2017
31

## Slide 32: Ion Torrent™ Workflow
Library
Preparation
Sequencing*
Data Analysis
Template Preparation*
Notes: Set expectations of the class:
There are several parts of the Ion workflow. The important phases are broken u here. The parts in blue we will go over in the lab together. This course does not cover the Library Prep portion of the workflow but we do offer several courses which cover this portion of the workflow.

## Slide 33: Ion Workflow Overview
Data Analysis
Clonal
Amplification
Isolate Positive
Ion Sphere™
Particles
Load Chip
and Sequence
Prepare
Library
10
10
DNA
A
Sequencing
D
Template Prep
C
Compatible Library Prep
B
Compatible Data
E
Notes: Ion Torrent Systems, Inc.
33

## Slide 34: Ion S5 & S5xlTM System - Torrent Server Inside
Torrent Suite™ Software
  Preloaded with Torrent Suite™ Software
  Converts raw signal to base calls
  Performs preliminary alignment to a reference genome allowing run quality assessment
  Torrent Browser plugins
  Hosts web portal for data review and distribution to collaborators
Notes: Torrent Server is the computer hardware running the Torrent Suite software
  pre-configured with software
  only way to access Torrent Suite software
  Contains GPU
Based on Dell T710 Server
USD $16,500
Euro €17,500
GBP £15,500
Part Number 700-2010-01
34

## Slide 35: Torrent SuiteTM Data Analysis Flow
Incorporation for
1 Flow (DAT)
Incorporation over
many flows (DAT)
Raw signals per flow (WELLS)
0.1 1.2 0.3 2.1 0.1 0.2 2.1 3.1 0.0
0.2 2.1 3.1 0.0 0.1 1.2 0.3 2.1 0.0
0.0 0.0 3.2 1.4 0.1 1.3 1.0 0.2 0.1
BAM
Base Calling
Signal
Processing
FASTQ
VCF
Unmapped BAM file
with base calls
& raw normalized signals
(optional)
For details on file formats & data analysis,
see the full documentation on the Ion Community.

## Slide 36: Ion Torrent™ : Semiconductor Sequencing for Life™
Support
Robert David
6178723352
Robert.David@thermofisher
ionsupport@lifetech.com
Call 800-955-6288 in USA
Bioinformatics support
ngs-amsupport@lifetech.com
Jingwei.Ni@thermofisher.com
Online info for Ion Torrent Systems Thermofisher Ion Community
The Chip is the Machine™
Notes: PLEASE CHANGE TECH SUPPORT NUMBER TO MATCH YOUR REGION’S CONTACT INFORMATION – THIS IS US-ONLY

## Slide 37
For Research Use Only. Not for use in diagnostic procedures.
Ion Torrent™ is a Thermo Fisher Scientific brand. © 2014 Thermo Fisher Scientific, Inc. All rights reserved. TaqMan is a registered trademark of Roche Molecular Systems, Inc., used under permission and license. All other trademarks are the property of Thermo Fisher Scientific and its subsidiaries.