## Slide 1: Ion Chef & S5/S5xl System overview & workflow

## Slide 2: Ion Chef Agenda
Ion ChefTM System overview:
Interactions with Ion ChefTM
  Setting up Ion ChefTM
  End-to-end process on Ion Chef™
  Sample and reagents tracking on Ion ChefTM
S5 System Overview
Planning & Executing a Run

## Slide 3
S5/S5 XL System Overview

## Slide 4: Ion Chef Agenda
Ion ChefTM System overview:
  Instrument
  Deck and functional modules
  Reagents and consumables
Interactions with the system
  Setting up Ion ChefTM
  End-to-end process on Ion Chef™
  Sample and reagents tracking on Ion ChefTM

## Slide 5: Ion Chef TM Video Overview
Notes: Hit shift and click in presentation mode to view the video on YouTube
https://www.youtube.com/watch?v=qpsd93d2mcc

## Slide 6: Workflow Overview

## Slide 7: Ion Chef TM: Automating your template preparation
Library Prep
Template Prep
Enrichment
Loading
Library Prep
Ion Chef TM
Notes: Simplifies the workflow, Minimizes sources of user-introduced variability, Saves time and labor, Supports sequencing preparation for the Ion PGM™ and Proton™ systems and chips

## Slide 8: Customers Typically Run Ion Chef™ Overnight
Day 1
Option 1
Morning
Afternoon
Option 2
Day 2
Ion Chef run is 10.5 hours. However, customers typically take advantage of programming feature that enables the overnight run (i.e. 17h+)
Notes: Overnight runs, chips ready in the morning. We are going to do option 1 in class

## Slide 9: Ion Chef™ System Orientation
Automated Template Prep, Enrichment and Loading

## Slide 10
Solution Cartridge Ambient Station
Reagent Cartridge Cold Station
New tip rack
Used tip rack.
Enrichment module
Tube centrifuges for ISP recovery and washing
Thermal cycler
Ion Chef™ System Orientation: Deck Layout
Thermal cycler lid
Chip centrifuge

## Slide 11: Ion Chef™ Kit Configuration
Ion PGM™ HiQ™ Chef Kit
Ion 540™ Kit – Chef
Ion 520™/530™ Kit - Chef
(8 reactions)
Template Prep &
Chip Loading on
Ion Chef™ system
Sequencing
on Ion PGM™ system and Ion S5/XL system
2 samples/run per cartridge set
Supports 200 and 400 bp RNA and DNA applications
Compatible with TSS 5.0 or higher
Notes: The new IC 200 kit includes template prep and sequencing kit or ease of ordering. 4 runs, 8 reactions.

## Slide 12: Ion Chef™ Reagent Cartridges Composition
4o C Reagent Cartridge
  Reagent Mix
  Enzyme Mix
  Primer B
  ISP
  Test Fragments
  Seq Primer
  Seq Polymerase
  NaOH
Ambient Temp Reagent Cartridge
  Annealing Buffer
  Loading Buffer
  Water
  IPA
  MyOnes
  Tween Solution
  Reagent B
  Recovery Solution
  Wash Solution
  Emulsion oil
Notes: Customer sample will be added to 4C cartridge

## Slide 13: Chef Workflow

## Slide 14: Diluting Libraries 520™/530™ Chips
Notes: Note: Prepare a fresh dilution of each library before use with the Ion Chef™ System,
and use the library dilutions within 48 hours.
Note: If running a control library, prepare the Human CEPH Control 200 Library,
obtained from the Ion S5™ Controls Kit (Cat. no. A27760), for use by diluting 1 μL into
52 μL Nuclease-free Water.

## Slide 15: Diluting Libraries 540™ Chips

## Slide 16: Setting up Ion Chef™

## Slide 17: Fully Automated Template Preparation
2 samples
2 Loaded chips
Ion S5XL™ Sequencing
Ion Chef™
Template Prep
Data
Notes: We will walk you through this training at a very high level first, and then dive into details

## Slide 18: Fully Automated Template Preparation
Step 1
Plan run
2 samples
2 Loaded chips
Ion S5XL™ Sequencing
Ion Chef™
Template Prep
Data

## Slide 19: Fully Automated Template Preparation
Load library samples into 4oC Reagent Cartridge
Step 2
2 samples
2 Loaded chips
Ion S5XL™ Sequencing
Ion Chef™
Template Prep
Data
Notes: Each kit has 8 reactions. Each 4C reagent cartridges

## Slide 20: Fully Automated Template Preparation
Step 3
Load Reagent Cartridges
4o C Reagent
Cartridge
Ambient Temp
Reagent Cartridge
2 samples
2 Loaded chips
Ion S5XL™ Sequencing
Ion Chef™
Template Prep
Data
Notes: Install both reagent cartridges

## Slide 21: Fully Automated Template Preparation
Load Plastic Consumables
Step 4
2 samples
2 Loaded chips
Ion PGM ™ Sequencing
Ion Chef™
Template Prep
Data
Notes: Add the tips and the empty tips rack in the back, add the plate and plate sealer in the middle. Add the enrichment tubes and recovery tubes

## Slide 22: Fully Automated Template Preparation
Attach adapters to chips, load chips
Step 5
2 samples
2 Loaded chips
Ion PGM ™ Sequencing
Ion Chef™
Template Prep
Data
Notes: Load both chips

## Slide 23: Fully Automated Template Preparation
When the deck is fully loaded, door closed and Desk Scan is complete, touch Next to display Data Destination
Confirm the instrument displays the correct kit name, chip types, and Planned Run. If the correct Planned Runs do not display, touch the drop-down menu to select the Planned Run for each chip, then touch Next.
Start Run
Step 6
2 samples
2 Loaded chips
Ion S5XL™ Sequencing
Ion Chef™
Template Prep
Data

## Slide 24: Run Options
The Ion Chef™ Instrument provides two options for obtaining quality control (QC) samples that can be used to assess templating efficiency.
Select Time or Pause and Start Run

## Slide 25: Fully Automated Template Preparation
2 Samples in
2 Loaded
Chips
Data
Ion Chef™
Ion PGM™
Sequencing
Step 8
Initialize
S5XL™
Step 7
Start Sequencing Run
remove chips from Ion Chef
remove adapter
load chip onto S5XL™
2 samples
2 Loaded chips
Ion S5XL™ Sequencing
Ion Chef
Template Prep
Data

## Slide 26: Fully Automated Template Preparation
2 Samples in
2 Loaded Chips
Data
Ion Chef™
Ion PGM™
Template Prep & Chip Loading
Sequencing
Post-run clean
2 samples
2 Loaded chips
Ion PGM Sequencing
Ion Chef
Template Prep
Data
Step 9
Press Clean button and follow instructions on screen
Location of waste
Note about liquid waste:
As there will be liquid waste in the used tip rack location, please take care not to spill on the deck. Volume of liquid waste: between 30-40mL. Do not over tilt the waste tip rack.

## Slide 27: Steps automated by Ion ChefTM workflow
1) Aqueous prep:
2) PCR Amplification:
Aqueous Prep
  HiQ™ equivalent
Emulsification
  Tip mix to make drops
PCR Amplification
  96-well thermal cycler
Notes: Emulsion PCR: Oil and Amp reaction are mixed to generate microscopic reaction vesicles.
2) Amplification:
Vesicles enter amplification plate, and undergoes PCR
Breaking: Vesicles from amp plate are transferred into centrifuges, where they are injected into breaking centrifuges for purification. ISPs are recovered through centripetal force
4) Enrichment:
Biotinylated ISPs are enriched using separation with magnetic streptavidin beads.
5) Sequencing biochem: sequencing primer is annealed to DNA on ISPs and polymerase is added
4) Chip Loading: Chips are loaded for PGM sequencing run

## Slide 28: Steps automated by Ion ChefTM workflow
3) Recovery:
4) Enrichment:
Recovery
  Bulk Breaking –oil removed
  Clean up similar to manual process
Enrichment
Notes: Emulsion PCR: Oil and Amp reaction are mixed to generate microscopic reaction vesicles.
2) Amplification:
Vesicles enter amplification plate, and undergoes PCR
Breaking: Vesicles from amp plate are transferred into centrifuges, where they are injected into breaking centrifuges for purification. ISPs are recovered through centripetal force
4) Enrichment:
Biotinylated ISPs are enriched using separation with magnetic streptavidin beads.
5) Sequencing biochem: sequencing primer is annealed to DNA on ISPs and polymerase is added
4) Chip Loading: Chips are loaded for PGM sequencing run

## Slide 29: Ion Chef™ Emulsion Breaking:
Recovery Solution
Emulsion
Oil
IPS are released from emulsion
vesicles via centrifugation through a layer of Recovery Solution. Oil and aqueous phase are removed by the robot during wash steps.
ISPs
Notes: Workflow Summary
Breaking is carried out in the white breaking centrifuge tubes for each sample.
1: Partial fill with Recovery Solution
2: Emulsion layered on top
3. Centrifugation forces vescicles downward, release/pellet ISPs
Remove Oil + Aq; leave pellet
5. Add Recovery Solutio to Step1 vol.
Repeat Steps 2 through 4

## Slide 30: Steps automated by Ion ChefTM workflow
5.) Chip Loading
Loading
  Primer annealing
  Chip loading
  Polymerase addition
  S5™ sequencing-ready
Notes: Emulsion PCR: Oil and Amp reaction are mixed to generate microscopic reaction vesicles.
2) Amplification:
Vesicles enter amplification plate, and undergoes PCR
Breaking: Vesicles from amp plate are transferred into centrifuges, where they are injected into breaking centrifuges for purification. ISPs are recovered through centripetal force
4) Enrichment:
Biotinylated ISPs are enriched using separation with magnetic streptavidin beads.
5) Sequencing biochem: sequencing primer is annealed to DNA on ISPs and polymerase is added
4) Chip Loading: Chips are loaded for PGM sequencing run

## Slide 31
QC sample Locations:
Sample 1
Sample 2
Qubit Sample – Reagent Cartridge
Pre Enriched Sample Only

## Slide 32: Sample / Reagent Tracking on Ion Chef™

## Slide 33
Automated sample tracking and pre-run check:
  Microscan Vision System (camera and barcode reader)
  Sample tracking functionality
  Barcoded chips, library samples
Setup check
  Scans all stations to ensure setup done correctly
  Scans during post-run clean as well
Sample / Reagent Tracking
Notes: Microscan Vision system for
  Barcode reading – samples, chips, reagents
  Automated calibration
  Load check
  Unload check

## Slide 34
Ion Chef™ System enables
sample tracking and LIMS/ITS integration
Plan Ion ChefTM run
Scan library tube in reagent cartridge and associate with customer sample library
Execute Ion ChefTM run
Vision system links the library barcode with the chip barcode
Review PGMTM data
Data from S5™chip is linked to the library in the Data tab
Plan
Monitor
Data

## Slide 35
S5/S5 XL System Overview

## Slide 36: Plug and Play Reagents
Temp Controlled Chip Clamp
Wash Solution
&
Waste Cartridge
(behind W2 Solution)
Sequencing Reagent
Cartridge
Large HD Touchscreen
Automated
Cleaning Solution
Standard Power
Notes: Large HD touchscreen – High quality
Temp control Chip Clamp – allows us to adjust temperature to optimize our chemistry
Automated cleaning solution – cleans after instrument run is complete
W2 solution – comes prefilled and pH-ed to optimal running condition. No need for high quality water
Waste cartridge – senses when waste is full and ask for your intervention to dump waste.
Sequencing cartridge – nucleotides are ready to go.
Finally- all you need is a 110 V plug outlet. We’ve removed the need for gas with our internal pump system and with our prefilled reagents high quality water is no longer a requirement.

## Slide 37
Single Use Consumables & Easy Tracking with RFID tags
RFID
tag
Tracking
Electronic Barcode
(1x use)
Reagent Cartridge
(1x use)
Wash
Solution
(1x use)
Waste Container
(Reusable)
Cleaning Solution
(4x use)
Universal kit for any chip type or read length
12 month Shelf-Life
Notes: Efuse?

## Slide 38
Ion S5™ XL System
Rapid sequencing and analysis for labs requiring more output or multiple runs per day
2.5 hr sequencing runs
Fast analysis. 1 hour – 5 hours, depending on chip type
Ion 520™
5 M Reads
Ion 530™
15-20 M Reads
Ion 540™
60-80 M Reads

## Slide 39: Easy and fast instrument setup
Install waste container, Wash Solution, Cleaning Solution and Nucleotide Cartridge
Install Chip
Select run plan, click Go!
Notes: Comment that there’s no autoph initiate time.

## Slide 40: Ion S5™/S5™ XL System Performance
 | 200bp Sequencing Time S5/S5 XL | 200bp Analysis Time* S5 XL | 200bp Analysis Time* S5 | Output | Reads | Read Length
Analysis time to BAM file
Ion 530™ Chip | 2.5 hr | ~2.5 hr | ~8 hr | 3-5 Gb | 15-20 M | Up to 400bp
Ion 540™ Chip | 2.5 hr | ~5 hr | ~16.5 hr | 10-15 Gb | 60-80 M | Up to 200bp
Ion 520™ Chip | 2.5 hr | ~1 hr | ~5 hr | 1-2 Gb | 3-5 M | Up to 400bp

## Slide 41: Ion Chef System for Automated Library & Template Prep with Ion S5 Systems Up to 40 Libraries Per Week At Optimized Workflow
Workflow | Unit | Day | Night | Day | Night | Day | Night | Day | Night | Day | Totals
Library Prep | Samples | 8 | 8 | 8 |  | 8 |  | 8 |  |  | 40
Templating | Samples |  |  |  | 16 |  | 16 |  | 8 |  | 40
Sequencing | Chip |  |  |  |  | 2 |  | 2 |  | 1 | 5
Mon
Tue
Wed
Thu
Fri
Assumes an 8 hour work day (with overnight run), 5 day work week
1 Ion Chef System and 1 Ion S5 System

## Slide 42: Plan and Execute a Run

## Slide 43: Torrent Browser Intro (Live Demo Run Plan)
http://10.56.120.36/plan/

## Slide 44
Torrent Browser Plan Creation
Ion PGM Hi-Q Chef Kit
Ion PGM Hi-Q Sequencing Kit
Notes: Select Ion Chef no OneTouch, IC 200 kits, and v2 chips only.

## Slide 45
Torrent Server Plan Creation
Scan or type sample tube barcode (included in kit)

## Slide 46: Ion Torrent™ : Semiconductor Sequencing for Life™
Support
Robert David
6178723352
Robert.David@thermofisher
ionsupport@lifetech.com
Call 800-955-6288 in USA
Bioinformatics support
ngs-amsupport@lifetech.com
Jingwei.Ni@thermofisher.com
Online info for Ion Torrent Systems Thermofisher Ion Community
The Chip is the Machine™
Notes: PLEASE CHANGE TECH SUPPORT NUMBER TO MATCH YOUR REGION’S CONTACT INFORMATION – THIS IS US-ONLY

## Slide 47
For Research Use Only. Not for use in diagnostic procedures.
Ion Torrent™ is a Thermo Fisher Scientific brand. © 2014 Thermo Fisher Scientific, Inc. All rights reserved. TaqMan is a registered trademark of Roche Molecular Systems, Inc., used under permission and license. All other trademarks are the property of Thermo Fisher Scientific and its subsidiaries.